## Slide 1
Module 1: Boolean & Digital Logic
EN605.204 Computer Organization

## Slide 2: Introduction
Boolean Logic
How do bits change/flow through digital circuits?
What is Boolean logic?
How do digital circuits implement Boolean logic?

## Slide 3: What is a “bit”?
Boolean Logic
Computer circuits are based on Boolean algebra
Boolean algebra operates on 1's and 0's
Claude Shannon showed the relationship between Boolean algebra and digital circuits in 1930's

## Slide 4: Logical NOT
Boolean Logic
Takes in a single bit as input and negates ("flips") it
Can be denoted using the ~ or ¬ character
Input (X) | Output (¬X)
0 | 1
1 | 0

## Slide 5: Logical OR
Boolean Logic
Takes two bits as input and outputs a 1 if either input was a 1
Can be denoted using the ∨, ⋃, or + character
Input (X, Y) |  | Output (X∨Y)
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 6: Logical AND
Boolean Logic
Takes two bits as input and outputs a 1 if both inputs were 1
Can be denoted using the ∧, ⋂, or * character
Input (X, Y) |  | Output (X∧Y)
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 7: Logical XOR
Boolean Logic
Two bits as input and outputs a 1 if exactly one input was a 1
Can be denoted using the ⊗ character
Input (X, Y) |  | Output (X⊗Y)
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 8: Logical NOR
Boolean Logic
Two bits as input and outputs a 1 if no inputs were a 1
Input (X, Y) |  | Output ¬(X∨Y)
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0

## Slide 9: Logical NAND
Boolean Logic
Two bits as input and outputs a 1 if at least 1 bit was a 0
Input (X, Y) |  | Output ¬(X∧Y)
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 10: Logic Gates
Boolean Logic

## Slide 11: Combinational Logic
Boolean Logic
Computer logic is implemented using physical "gates"
Gates can be strung together to build more complex logic
Example: AND(OR(W, X), OR(Y, Z))
  Input: {0, 0, 0, 1}
  = AND(OR(0, 0), OR(0, 1))
  = AND(0, 1)
  = 0

## Slide 12: Universal Logic Gates
Boolean Logic
NOR and NAND gates are "universal"; they can simulate any logical operation

## Slide 13: Laws of Boolean Logic
Boolean Logic
Input (X, Y) | Output ¬(X∧Y) | 
Identity | X∧1 = X | X∨0 = X
Complementation | X∧¬X = 0 | X∨¬X = 1
Double Negation | ¬(¬X) = X | 
Idempotent | X∧X = X | X∨X = X
Dominance | X∧0 = 0 | X∧1 = 1
Commutative | X∧Y = Y∧X | 
Associative | X∧Y∧Z = X∧(Y∧Z) = (X∧Y)∧Z | 
Distributive | X∧(Y∨Z) = (X∧Y)∨(X∧Z) X∨(Y∧Z) = (X∨Y)∧(X∨Z) | 

## Slide 14: DeMorgan's Law
Boolean Logic
(X OR Y) and (X AND Y) are called "propositions"
¬(X OR Y) = ¬X AND ¬Y
  The proposition X OR Y fails if X and Y are false
  Ex: "I don't like the Cowboys (X) or Patriots (Y)" = "I don't like the Cowboys (X) and I don't like the Patriots (Y)."
¬(X AND Y) = ¬X OR ¬Y
  The proposition fails if either X is false or Y is false
  Ex: "I don't want a sandwich unless it has both ham (X) and cheese (Y)." = "I don't want a sandwich if it doesn't ham (X) or if it doesn't have cheese (Y)."